| SPECIFICATION FOR APPROVAL |
| --- |
| CUSTOMER ： CUSTOMER PART NO： |
| SUPPLIER： JIAXING GLEAD ELECTRONICS CO.,LTD. SUPPLIER PART NO： DAM1595A4H10LC01_XW03_K3M DESCRIPTION： 3.0-5.0V/8.5mA(3V)/28dB/3M（L）/FAKRA-C REMARKS： |
| Customer Signature : Customer Seal: Supplier Signature: Supplier Seal : NOTE: Please return this copy as a certification of your approval！ |
| Prepared by： Zhu huiguang | Formed On： 2017.11.03 | Add | No.66 ZhengyuanRoad,Tanghui Industrial Zone, Jiaxing, Zhejiang, China |
|  |  | Tel | +86-573-83651818 |
|  |  | Fax | +86-573-83651858 |
| VERSION DATE REVISION DESCRIPTION PREPARED CHECKED APPROVED V1.0 2017/11/03 NEW ISSUED Zhu huiguang Wu Zhijun Gao Sheng |

| PRODUCT NAME | Prepared date | Page |
| --- | --- | --- |
| DAM1595A4H10LC01_XW03_K3M | 2017.11.03 | 3/8 |
| Prepared by | Checked by | Approved by |
| Zhu huiguang | Wu Zhijun | Gao sheng |
| 1、Electrical Characteristics 1.1Antenna 1 Antenna model DAS1575（25*25*4） 2 Frequency Range GPS:1575.42MHz±1.023 MHz ；GLNASS：1602MHz±6 MHz 3 V.S.W.R 1.5:1 4 Band Width > 8 MHz for GPS ； > 8MHz for GLONASS 5 Impedance 50 ohm 6 Gain 4.5dBic Based on7×7cm ground plane 7 Polarization RHCP 1.2 LNA 1 Frequency Range GPS:1575.42MHz±1.023 MHz ；GLNASS：1602MHz±6 MHz 2 DC Voltage 3.0-5.0V 3 Gain 28±3dB 4 Outband Regection (Absolute value) ≥30dB(fo+100MHz) ≥30dB(fo-100MHz) 5 Output VSWR 2.0 6 Noise Figure 1.5 7 DC current 8.5±3mA (at3.0V) 1.3 Overall (Complete module including RF connector) 1 Frequency Range GPS:1575.42MHz±1.023 MHz ；GLNASS：1602MHz±6 MHz 2 Output VSWR 2.0 3 Impedance 50Ω |

| PRODUCT NAME | Prepared date | Page |
| --- | --- | --- |
| DAM1595A4H10LC01_XW03_K3M | 2017.11.03 | 4/8 |
| Prepared by | Checked by | Approved by |
| Zhu huiguang | Wu Zhijun | Gao sheng |
| 2、Patch Test curve |

| PRODUCT NAME | Prepared date | Page |
| --- | --- | --- |
| DAM1595A4H10LC01_XW03_K3M | 2017.11.03 | 5/8 |
| Prepared by | Checked by | Approved by |
| Zhu huiguang | Wu Zhijun | Gao sheng |
| 3、LNA Test curve(Test condition: DC 3.0V) |

| PRODUCT NAME | Prepared date | Page |
| --- | --- | --- |
| DAM1595A4H10LC01_XW03_K3M | 2017.11.03 | 6/8 |
| Prepared by | Checked by | Approved by |
| Zhu huiguang | Wu Zhijun | Gao sheng |
| 4、Structure (unit：mm) 未注公差：±0.3mm L=300±10CM |
| PRODUCT NAME | Prepared date | Page |
| DAM1595A4H10LC01_XW03_K3M | 2017.11.03 | 7/8 |
| Prepared by | Checked by | Approved by |
| Zhu huiguang | Wu Zhijun | Gao sheng |
| 5、Material No Part Name SPEC 1 Antenna Dielectric Ceramics 2 PCB FR4 3 Shielding Tinplate 4 RF Cable RG174 5 RF Connector FAKRA-C 6 Circular magnets NdFeB 6、Environment Condition 1 Working Temp -40℃~+85℃ 2 Storage Temp -40℃~+85℃ 3 Vibration Sine sweep 1g(0-p) 10~55~10Hz each axis 4 International Protection IP66 7、 Packing（If there are other customers packaging requirements specified in the order） Each carton includes 100 PCS antenna，Each lattice put 2PCS antenna, the size of carton is 630 * 460 * 105 mm. |

| PRODUCT NAME | Prepared date | Page |
| --- | --- | --- |
| DAM1595A4H10LC01_XW03_K3M | 2017.11.03 | 8/8 |
| Prepared by | Checked by | Approved by |
| Zhu huiguang | Wu Zhijun | Gao sheng |
| 8、Note This product specification guarantees the quality of our product as a single unit. Please make sure that your product is evaluated and confirmed against your specifications when our product is mounted to your product. The product will get free warranty for three months since the date of purchase users operate in the correct way; users will have to pay cost of the materials and maintaining fee out of the condition. 3、Electrostatic sensitive device.Observe precautions for handling. |